## Slide 1
MPLS in an IPv6-Only Network
Doable or a “Bridge Too Far”?
Berislav Todorovic, Juniper Networks
btodorovic@juniper.net

## Slide 2: Agenda
Intro – the IPv6 prelude and the MPLS fugue ...
IPv6 and MPLS – current solutions for the IPv6 edge of an IPv4 core:
    6PE, 6VPE, IPv6-over-TE tunnels ... or native IPv6
MPLS over an IPv6-only core – MPLS transport challenges:
    LDPv6, RSVP-TEv6, BGP-LU(v6), SPRINGv6
MPLS service challenges in an IPv6 core:
    L3 VPN
    L2 VPN – VPLS/VPWS/EVPN
    MVPN
Can we get rid of IPv4 actually ???

## Slide 3: Prelude – IPv6 Takes up ...
SPs introduce IPv6 to please the nerds
RFC 6540 - IPv6 Support Required for All IP-Capable Nodes (2012!)
ripe-554 - Requirements for IPv6 in ICT Equipment (2010-2012)
IAB Statement on IPv6 (2016):
  We recommend that all (future) networking standards assume the use of IPv6, and be written so they do not require IPv4.
Will the Internet world (eventually?) default to IPv6?
because they have no other choice (out of “v4 stock”)

## Slide 4: Fugue - MPLS is Still Out There ...
MPLS - invented in the late 1990s
Envisaged for an odd use case (ATM/IP interworking).
But we use it for other reasons today:
  MPLS VPN
  Traffic Engineering
  Fast traffic restoration (FRR)
Can’t we do it with: overlays, underlays ... ^.*lays$ ...
MPLS doesn’t give up that easy, like its A** predecessor:
  Mobile operators just love it! 
  Reason – SDH-grade fast restoration, TE ...
Problem – it was developed assuming an IPv4 core
as its foundation!

## Slide 5: Prelude Again –IPv4 Packet Forwarding
Although, IPv6 is the same thing ...
14.3.3.3
IP 10.1.1.1
3
2
1
11
21
1
2
3
IP 10.1.1.1
IP 10.1.1.1
IP 10.1.1.1
Destination | Intf
10.1.1.1 | 1
11.2.2.2 | 2
14.3.3.3 | 3
Destination | Intf
14.3.3.3 | 1
11.2.2.2 | 2
10.1.1.1 | 3
Destination | Intf
10.1.1.1 | 11
11.2.2.2 | 21
14.3.3.3 | 31
31
11.2.2.2

## Slide 6: Prelude Again –IPv6 Packet Forwarding
14.3.3.3
IP 2001:a:b:8::1
3
2
1
11
21
1
2
3
IP 2001:a:b:8::1
IP 2001:a:b:8::1
IP 2001:a:b:8::1
Destination | Intf
2001:a:b::/48 | 1
2a01:c::/32 | 2
2b01:80:1::/56 | 3
31
11.2.2.2
Destination | Intf
2a01:c::/32 | 2
2b01:80:1::/56 | 1
2001:a:b::/48 | 3
Destination | Intf
2001:a:b::/48 | 11
2a01:c::/32 | 21
2b01:80:1::/56 | 31

## Slide 7: Interlude – The Label ...
Add a 4 byte tag to each IP packet ...
IP Packet
L2 Header
IP Packet
L2 Header
IP Packet
L2 Header
TTL
Label (20 bits)
CoS
S
4 bytes
MPLS Header
RFC3031 just says “IP Packet”
Can be BOTH v4/v6 ...
... or even an Ethernet frame (L2 packet)!

## Slide 8: Fugue – MPLS Label Switching
50
Classical IP Forwarding (again IPv4 or IPv6 – doesn’t matter ... yet ...)
14.3.3.3
10.1.1.1
3
2
1
11
21
1
2
3
10.1.1.1
31
11.2.2.2
Lb-Out
50
52
57
IFin | LB-in
1 | 50
IFin | LB-in | IFout | Destination
31 | 20 | 11 | 10.1.1.1
10.1.1.1
50
10.1.1.1
20
Destination | Intf
10.1.1.1 | 1
11.2.2.2 | 2
14.3.3.3 | 3
10.1.1.1
50
IFout | LB-out
3 | 20
20
Label-Switchd Path (LSP)
Can this be IPv6 too?
Of course, but ...

## Slide 9: Label Stacking
Packet
L2 Header
IP Packet
L2 Header
Packet
L2 Header
TTL
Label (20 bits)
CoS
S
4 bytes
MPLS Header
Adding more labels to the packets ...
Packet
L2 Header
IP Packet
L2 Header
Packet
L2 Header
TTL
Label (20 bits)
CoS
S
4 bytes
MPLS Header
Packet
L2 Header
L1
L2
L3
Ln
4*n bytes
Label Stack

## Slide 10: Coda - MPLS L3 VPNs – Forwarding Plane
Using the label-stacking technique to create VPNs
P
P
P
PE 2
VPN A
Site 3
VPN A
Site 1
VPN B
Site2
VPN B
Site 1
PE 1
PE 3
VPN A
Site2
CE – A1
CE – B1
CE – A3
CE – A2
CE – B2
CE1 – A2
10.1.1.1
12
10.1.1.1
11
10.1.1.1
11
10.1.1.1
12
51
51
Service
Label
Service
Label
Transport
Label

## Slide 11: MPLS L2 VPNs – Forwarding Plane
Pushing Ethernet frames from A to B (“pseudowires”)

## Slide 12: Problem – Label Signaling (Control Plane)!
50
Unsolicited Downstream Label Distribution
14.3.3.3
3
2
1
11
21
1
2
3
31
11.2.2.2
IFin | Dest | IFout | LB-out
3 | 10.1.1.1 | 1 | 50
2 | 11.2.2.2 | 2 | 52
IFin | LB-in
1 | 50
IFin | LB-in | IFout | Destination
31 | 20 | 11 | 10.1.1.1
Destination | Intf
10.1.1.1 | 1
11.2.2.2 | 2
14.3.3.3 | 3
10.1.1.1
50
IFout | LB-out
3 | 20
20
10.1.1.1
Label=20
10.1.1.1
Label=20
10.1.1.1
Label=50
10.1.1.1
Label=50
Label signaling
uses IPv4 !!!

## Slide 13: MPLS VPN Site Signalling (Control Plane)
Exchanging IP network information among VPN sites
B
PE1
IP/MPLS Backbone
PE2
PE3
CE
PE4
A
CE
A
CE
B
CE
192.0.3.0 /24
RR
100.64.32.0/ 24
192.0.4.0 /22
100.71.0.0 /23
MP-BGP
(over IPv4)
?
?

## Slide 14: MPLS Control Plane – Signaling ...
MPLS Transport Signaling – determines transport label values:
  LDP
  RSVP-TE
  BGP-LU
  SPRING (Segment Routing)
Service Signaling – determines service label values and routing:
  Depends on service
  MPLS L3 VPNs – use MP-BGP
  MPLS L2 VPNs – can use either MP-BGP or LDP
  6PE / 6VPE (IPv6-over-MPLS) – uses MP-BGP
Problem – most of those protocols assume an IPv4 core!
Even IPv6 services running over MPLS ... WHY?

## Slide 15: IPv6 in MPLS Networks – Solutions So Far
MPLS was created based assuming an underlying IPv4 infrastructure!
Remember, this was in 1998:
  No IPv4 address space issues
  No widespread broadband Internet connectivity.
  No smartphones, tables, phablets ... .*blets$
  No Instagram, Facebook, Linkedin, Snapchat ...
Still, MPLS operators pushed to provide IPv6 connectivity since Day 1.
Standard industry solutions based on an IPv6-agnostic core.
“Do not touch the (IPv4) core, run IPv6 on the edge only!”
Options:
    Native IPv6 in the core (non-label switched)
    6PE (RFC4798)
    6VPE (RFC4659)
<sarcasm>
How could we ever live without those ... ???
</sarcasm>

## Slide 16: 6PE (IPv6 Provider Edge) Architecture (RFC4798)
IPv6-agnostic area
MPLS core
IPv6 Edge (6PE)
IPv6
customer
IPv6
customer
EBGP
between
IPv6
endpoints
EBGP
betwen
IPv6
endpoints
IPv6
IPv6
Forwarding plane
Control plane
IPv4
MPLS
MP-iBGP - between IPv4 endpoints
LDP (or RSVP) - between IPv4 endpoints
IGPv4 (OSPF, IS-IS etc.)

## Slide 17: But what if we pull the IPv4 plug ???
IPv4

## Slide 18: Why Pull the IPv4 Plug?
Running an IPv6-only core – why not?
IPv4 can move to the edges (4PE instead of 6PE).
Trials done in the past – e.g. Peter Lothberg’s TeraStream:
  https://ripe67.ripe.net/presentations/131-ripe2-2.pdf
Operationally simple:
  Maintain only one set of ACLs.
  Manage it only via IPv6
  Avoid overlaps on management IP addresses – e.g. for zillions CPEs ...
Nice thought ... but nightmare for MPLS!

## Slide 19: Test Topology
with permission of the author Krzysztof Szarkowicz, this example was taken from the book (with slight modifications):
A. Sánchez-Monge and K. Szarkowicz, MPLS in the SDN era, 1st ed. O'Reilly Media Inc, 2015.
cpe1
cpe2
cpe3
cpe4
pre1
pre2
pre3
pre4
cr1
cr2
rr1
rr2
2
3
4
5
6
7
8
9
10
11
12
15
13
14
16
17
18
19
20
n = circuit number
IPv6 P2P: 2001:8:8:hex(n)::/64
r = router number
IPv6 P2P: 2001:8:0::hex(r)/128
1
2
12
13
4
5
10
11
6
7
8
9
r
n

## Slide 20: Traceroute – IPv6 in Global Routing Table
beri@cpe2> show route table inet6.0 terse
A V Destination P Prf Metric 1 Metric 2 Next hop AS path
* ? 2001:8::/32 B 170 100 65000 I
>2001:8:8:2::2
* ? 2001:222::1/128 D 0 >lo0.0
* ? 2001:444::/32 B 170 100 65000 65444 I
>2001:8:8:2::2
beri@cpe2> traceroute 2001:444::1 source 2001:222::1
traceroute6 to 2001:444::1 (2001:444::1) from 2001:222::1, 64 hops max, 12 byte packets
1 pre2 (2001:8:8:2::2) 141.331 ms 99.055 ms 129.311 ms
2 pre1 (2001:8:8:5::1) 89.134 ms 81.426 ms 56.412 ms
MPLS Label=300160 CoS=0 TTL=1 S=0
3 cr1 (2001:8:8:6::2) 198.055 ms 172.842 ms 184.104 ms
MPLS Label=300448 CoS=0 TTL=1 S=0
4 pre3 (2001:8:8:10::1) 6.077 ms 7.645 ms 5.673 ms
5 2001:444::1 (2001:444::1) 15.286 ms 8.099 ms 10.956 ms

## Slide 21: Traceroute – IPv6 in a VPN
beri@cpe1> show route table inet6.0 terse
A V Destination P Prf Metric 1 Metric 2 Next hop AS path
* ? 2001:db9::1/128 D 0 >lo0.0
* ? 2001:dba::/32 B 170 100 65000 65002 I
>2001:8:f:1::
beri@cpe1> traceroute 2001:dba::1 source 2001:db9::1
traceroute6 to 2001:dba::1 (2001:dba::1) from 2001:db9::1, 64 hops max, 12 byte packets
1 2001:8:f:1:: (2001:8:f:1::) 84.542 ms 87.228 ms 70.557 ms
2 pre1 (2001:8:8:5::1) 83.897 ms 57.609 ms 150.652 ms
MPLS Label=300160 CoS=0 TTL=1 S=0
MPLS Label=16 CoS=0 TTL=1 S=1
3 cr1 (2001:8:8:6::2) 105.846 ms 110.714 ms 107.287 ms
MPLS Label=300448 CoS=0 TTL=1 S=0
MPLS Label=16 CoS=0 TTL=2 S=1
4 2001:8:f:2:: (2001:8:f:2::) 190.653 ms 190.920 ms 67.796 ms
5 2001:dba::1 (2001:dba::1) 35.943 ms 20.132 ms 11.525 ms

## Slide 22: However ...
Many things still rely on IPv4
Transport signaling (LDPv6) is resolved, however ...
Service signaling is not:
  None of the vendors support MP-BGP over IPv6 endpoints
  Even for VPNv6 (IPv6 VPN) address family BGP requires IPv4 endpoints!
  L2VPN – both LDP- and BGP-signaled L2VPNs can run over IPv6 infra
  However, most vendors mostly implemented the IPv4-only version.
  MVPN using P2MP LSPs – will require updates for IPv6 ...
Implementation or standards issue?
Well ...

## Slide 23: RFC7439
[RFC7439] George, W., Ed., and C. Pignataro, Ed., "Gap Analysis for Operating IPv6-Only MPLS Networks", RFC 7439, DOI 10.17487/RFC7439, January 2015, <http://www.rfc-editor.org/info/rfc7439>.

## Slide 24: RFC7439 Gap Summary
+---------+---------------------------------------+-----------------+
| Item | Gap | Addressed in |
+---------+---------------------------------------+-----------------+
| LDP | LSP mapping, LDP identifiers, LDP | [LDP-IPv6] |
| S.3.2.1 | discovery, LDP session establishment, | |
| | next-hop address, and LDP TTL | |
| | security | |
+---------+---------------------------------------+-----------------+
| mLDP | Inherits gaps from LDP, RFC 6512 | Inherits |
| S.3.2.2 | [RFC6512] | [LDP-IPv6], |
| | | additional |
| | | fixes TBD |
+---------+---------------------------------------+-----------------+
| GMPLS | RFC 6370 [RFC6370] Node ID derivation | TBD |
| S.3.2.6 | | |
+---------+---------------------------------------+-----------------+
| L2VPN | RFC 6074 [RFC6074] discovery, | TBD |
| S.3.3.1 | signaling | |
+---------+---------------------------------------+-----------------+
| L3VPN | RFC 4659 [RFC4659] does not define a | TBD |
| S.3.3.2 | method for 4PE/4VPE | |
+---------+---------------------------------------+-----------------+
| OAM | RFC 4379 [RFC4379] No IPv6 multipath | [IPv6-RAO] |
| S.3.4 | support, no IPv6 RAO, possible | |
| | dropped messages in IP version | |
| | mismatch | |
+---------+---------------------------------------+-----------------+
| MIB | RFC 3811 [RFC3811] no IPv6 textual | [MPLS-TC] |
| Modules | convention | |
| S.3.5 | | |
+---------+---------------------------------------+-----------------+

## Slide 25: Conclusion
If you run MPLS, you’ll still need IPv4 ...
Standards will fill the gaps to run MPLS in IPv6-only networks.
Implementations will certainly follow, but not that quickly.
Will newer technologies (e.g. SPRINGv6 w/ overlay VPNs) phase out MPLS?
Possibly ... but not that fast either ...