## Slide 1: PC based software router
Nenad Krajnović, SOX CTO
krajko@sox.rs
Goran Slavić, SOX Chief Engineer
gslavic@sox.rs
SEE 6
Budva, Montenegro

## Slide 2: BGP routing table today
 | IPv4 Table | IPv4 Prediction
Jan 2013 | 441,172 | 
Jan 2014 | 488,011 | 
Jan 2015 | 529,806 | 
Jan 2016 | 586,879 | 
Jan 2017 | 645,974 | 
Jan 2018 |  | 697,000
Jan 2019 |  | 751,000
Jan 2020 |  | 806,000
Jan 2021 |  | 861,000
Jan 2022 |  | 915,000
Source: https://labs.apnic.net/?p=952

## Slide 3: How to buy “cheap” BGP router?
L3 switch with 1G/10G ports cost from 2500$
  Typically, they support ~12k prefixes.
  Only some of them have BGP implemented.
Classical router cost from 10k$ and they can support full BGP table.
  Typically, they do not have 10G ports and the throughput is 2,5 Gbps

## Slide 4: “Full feature” router
Ports: 1G/10G
Routing: BGP, OSPF, …
Performances: 100Gbps, 130Mpps
Price: from 50k$ ↗

## Slide 5: Alternative solution
Build your own router based on standard PC hardware
What are the limitations?
  3 Mpps
  Throughput depends on packet length, between 1,5Gbps and 36Gbps
But:
  Low price!
  Unlimited number of prefixes!

## Slide 6: What we need?
PC based server with PCIe 3.0 slot (10G can work on 2.0 slot), advanced Intel CPU, from 2GB RAM
Network Interface Card with 10G ports or 40G ports (one 40G is enough)
CentOS (or whatever you like from *nix family)
Quagga (Cisco-like CLI) or BIRD

## Slide 7: Setup (#1/2)
Ethernet ports should be configured in trunk mode (not necessary, depends on topology).
Activate IPv6 forwarding (preferable).
Disable NetworkManager.service.
Disable gnome-desktop.
Install pciutils (for load balancing of IRQs).

## Slide 8: Setup (#2/2)
Install net-snmp (for remote monitoring).
Install openssh (for remote management).
Any addition utility to monitor the router

## Slide 9: Network FINE TUNNING (#1/7)
Modification of /usr/lib/sysctl.d/00-system.conf – disable netfilter on bridges.
  net.bridge.bridge-nf-call-ip6tables = 0
  net.bridge.bridge-nf-call-iptables = 0
  net.bridge.bridge-nf-call-arptables = 0

## Slide 10: Network FINE TUNNING (#2/7)
Modification of /usr/lib/sysctl.d/50-default.conf
  net.ipv4.conf.default.rp_filter = 0
  net.ipv4.conf.all.rp_filter = 0

## Slide 11: Network FINE TUNNING (#3/7)
Modification of /etc/sysctl.d/99-sysctl.conf
  net.ipv6.conf.lo.forwarding = 1
  net.ipv4.tcp_syncookies=1
  net.ipv4.conf.default.rp_filter = 0
  net.ipv4.conf.default.accept_source_route=0
  net.ipv4.ip_nonlocal_bind = 1
  kernel.shmmax=68719476736
  kernel.msgmax=65536
  kernel.msgmnb=65536
  kernel.sysrq=0
  kernel.shmall=4294967296
  kernel.core_uses_pid=1

## Slide 12: Network FINE TUNNING (#4/7)
echo 0 > /proc/sys/net/ipv4/conf/default/rp_filter
echo 0 > /proc/sys/net/ipv4/conf/all/rp_filter

## Slide 13: Network FINE TUNNING (#5/7)
net.ipv4.conf.all.forwarding = 1
net.ipv4.conf.all.rp_filter = 0
net.ipv4.conf.all.arp_announce = 2
net.ipv4.conf.all.arp_ignore = 1
net.ipv6.conf.all.autoconf = 0
net.ipv6.conf.all.accept_ra = 0
net.ipv6.conf.all.forwarding = 1
net.ipv4.conf. default.forwarding = 1
net.ipv4.conf.default.rp_filter = 0
net.ipv4.conf.default.arp_announce = 2
net.ipv4.conf.default.arp_ignore = 1
net.ipv4.conf.default.arp_filter = 0
net.ipv6.conf.default.autoconf = 0
net.ipv6.conf.default.accept_ra = 0
net.ipv6.conf. default.forwarding = 1
Settings for interfaces:

## Slide 14: Network FINE TUNNING (#6/7)
Per VLAN configuration (if it is necessary):
  net.ipv4.conf.XXXX/VLAN.forwarding = 1
  net.ipv4.conf.XXXX/VLAN.rp_filter = 0
  net.ipv4.conf.XXXX/VLAN.arp_announce = 2
  net.ipv4.conf.XXXX/VLAN.arp_ignore = 1
  net.ipv4.conf.XXXX/VLAN.arp_filter = 0
  net.ipv6.conf.XXXX/VLAN.autoconf = 0
  net.ipv6.conf.XXXX/VLAN.accept_ra = 0
  net.ipv6.conf.XXXX/VLAN.forwarding = 1

## Slide 15: Network FINE TUNNING (#7/7)
Optional automatic IPv6 address assignment prevention:
  echo 0 > /proc/sys/net/ipv6/conf/em1/autoconf
  echo 0 > /proc/sys/net/ipv6/conf/em1/accept_ra

## Slide 16: Practical implementation
HP ProLiant DL 180 G6
2 x Intel Xeon CPU X5675 @ 3.07GHz (6-core processor)
12GB RAM
2 x (2x10G Ethernet controller 82599ES) – total 40G interface
Total cost of HW: from 1000$ (HP server on Ebay) + from 300$ 10G NIC = ~1600$

## Slide 17: Performances Total traffic on router interfaces

## Slide 18: Performances Total packets on router interfaces

## Slide 19: Performances Total load of the router

## Slide 20: Performances Total load of the router CPUs

## Slide 21: Limitations
When traffic reached 3Mpps, router started with jitter and increased packet latency.
The reason is implementation of packet handling in Linux kernel.
DPDK, netmap and Vector Packet Processing are work in progress to overcome this problem.

## Slide 22: Test with 40G interface
Setup for the test – hand-made PC server (total ~1000$):
  Motherboard: ASUS P8H77-V
  CPU: Quad core Intel(R) i7-3770 CPU @ 3.40GHz
  RAM: 12GB
  NIC: 2x40G Intel Ethernet Controller XL710 for 40GbE QSFP+
Server stopped forwarding traffic after 20 hours because of problem with NIC driver. Reload of the driver temporary solved the problem.
Till stopping, everything works perfect.

## Slide 23: Conclusions:
Viable solution for the traffic up to 3Mpps.
Total throughput in Gbps depends on size of the packets.
Quagga provides full BGP functionality with “unlimited” number of prefixes.
If we “forget the price of human work”, very cheap solution!

## Slide 24: PC based software router
Nenad Krajnović, SOX CTO
krajko@sox.rs
Goran Slavić, SOX Chief Engineer
gslavic@sox.rs
SEE 6
Budva, Montenegro