## Slide 1: Software defined networking: Experimental research on QoS
RIPE SEE6 Regional Meeting, Budva, 13.06. 2017.
UNIVERSITY OF MONTENEGRO
FACULTY OF ELECTRICAL ENGINEERING
Slavica Tomovic

## Slide 2: Motivation: QoS problems
Internet today:
  “Best-effort” service model
  Different types of traffic are treated in the same way
  There is no performance guarantees
Trend: A constant growth in demand for multimedia applications
  Video streaming, VoIP, video conferencing, online gaming, IPTV...
  Different QoS requirements: bandwidth, delay, jitter, packet loss...
  “Best-effort” is not good enough!

## Slide 3: General outlook on SDN
The key concepts:
Separation od the control plane from the data plane
Centralized control plane
Programmable devices
SDN benefits:
Flexible control
Traffic engineering
Simplified management
Global view of the network state
Specialized hardware
Ap
Ap
Ap
Specialized hardware
Ap
Ap
Ap
Specialized hardware
Operating system
Operating system
Operating system
Ap
Ap
Ap
Network Operating System
Application
Application
Application
NorthBound API
“open” API (e.g. OpenFlow)

## Slide 4: QoS controller design
Match fields
Counters
Actions
In Port
Src MAC
Dst MAC
Eth Type
Vlan Id
IP Tos
IP Prot.
IP Src
IP Dst
TCP Src Port
TCP Dst Port
L2
L3
L4
Flow rules
Modules:
Resource monitoring
Routing
Resorce reservation
Admission control

## Slide 5: QoS controller design
Resource monitoring
  Collects information about the current state of the network
  Topology discovery and statistics gathering
Resource reservation
  Reserves bandwidth for priority traffic flows by configuring ouput queus of OpenFlow switches
  HTB scheduling algorithm
  For each QoS flow minimum and maximum rate is configured according to its requirements
  Special buffer is created for best-effort traffic

## Slide 6: QoS controller design
Route computation
  QoS algorithm
    Bandwidth-delay constrained algorithm
  Best-effort algorithm
    Routing metric based on estimated level of the link load
    Rerouting algorithm is run when link load reaches the certain treshold value:
      Congestion treshold: 80% of link capacity
      Goal: bring the link usage below the threshold level with as few as possible reroutings.

## Slide 7
QoS
List of priority flows
50Mbit/s
Source | Destination | Demand
8.8.8.2 | 8.8.8.5 | 50Mbit/s
OpenMont controller
Tok | Action
Flow table of switch 1
Not a priority flow! Send packets to buffers with id 0, over the route switch 1 – switch 2
Instructon
Instrution
Flow | Action
Flow table of switch 2
8.8.8.1 – 8.8.8.7
8.8.8.1 – 8.8.8.7
Go to buffer 0 of port 1
Go to buffer 0 on port 2
Priority flow! Delete best-effort entries from the flow tables!
Create new buffers on the route: switch 1 – switch 2 and send priority packets to them
8.8.8.2 – 8.8.8.5
Go to buffer 1 of port 1
8.8.8.2 – 8.8.8.5
Go to bafer 1 of port 1
p.1
p.1
p.2
Link capacity 100Mbit/s !!!
It is not a priority flow! The shortest route is congested. Go over longer route!
Go to buffer 0 of port 2
p.2
Instruction

## Slide 8: Experimental results
SDN QoS model
IntServ
QoS experiment
Best-effort experiment

## Slide 9: Testbed
OpenFlow switches:
  HP ProCurve
  Pica 8
  OpenvSwitch software switches
  NetFPGA boards
12 X
=4X
Notes: Like other Linux-based machines with OVS installed, Pica8 could be logically partitioned into multiple independent OpenFlow switches with dedicated physical interfaces. For our purpose, Pica8 is virtualized into twelve virtual switches (colored in orange in Fig. 1). These virtualized switches are managed in the same way as OVS switches, but with the possibility to store the flow entries in the hardware flow tables.
HP ProCurve 6600 switches cannot be virtualized in the same way as Pica8. While white box switches allow creation of multiple virtual switches and assignment of physical ports to them, in order to create multiple virtual OpenFlow switches from HP ProCurve 6600, separate VLAN (Virtual Local Area Network) has to be configured for each virtual switch. OpenFlow virtual switches are independent and have their own configuration and connection towards the OpenFlow controller. In our testbed, HP ProCurve is logically separated into four OpenFlow virtual switches, colored in green

## Slide 10: Controller benchmarking
The most popular open-source SDN controllers:
ONOS
FLOODLIGHT
POX
Latency tests
Throughput tests
Cbench — Controller benchmarking tool
Notes: Cbench emulates OpenFlow switches which communicate with controller. As input arguments it takes a number of switches that should be emulated, number of hosts per switch and the controller's address. It supports two working modes: latency and throughput mode. In latency mode, it sends PACKET_IN messages to the controller. These messages are used by OpenFlow protocol to inform the controller when a packet received by a switch does not match any entry in the flow table. As a response, controller generates FLOW_MOD message, which installs a new entry in the flow table. If a controller cannot make routing decision, (e.g. because packet destination is unknown), it will just instruct switch to drop or flood a packet via PACKET_OUT message, depending on the control application used. When Cbench works in latency mode, it measures the time taken to handle a single packet. The next PACKET_IN message is generated only after a corresponding response is received from the controller. In throughput mode, the emulated switches send as many PACKET_IN messages as possible to the controller, making sure that the controller always has messages to process [6]. The result of both, throughput and latency tests, are expressed in number of received responses per second. In order to examine how multi-threading impacts controllers' performances, we conducted multiple experiments where controllers have been run with different number of threads (using taskset Linux command).

## Slide 11: EVALUATION results
Cbench throughput test:
Cbench latency test:

## Slide 12: Conclusions
The distributed control plane hinders development of efficient QoS mechanisms
SDN architecture enables implementation of efficient network monitoring mechanisms
QoS-aware design of SDN controller promisses better QoS to both, priority and best effort traffic flows
Scalability of SDN controller is an important issue

## Slide 13
Thank you!
Questions?