## Slide 1: IoT Turning Evil
Dr Ivana Tomić and Prof. Julie A. McCann
Email: i.tomic@imperial.ac.uk
Imperial College London
PETRAS Internet of Things Research Hub

## Slide 2
“highly decentralised algorithms, protocols, cross-layered solutions to wireless sensor networks”
Some of our research projects: ICRI sustainable connected cities, security of IoT/CPS, anomaly detection, energy neutral operation, distributed adaptive control in CPS…
Example of on-site low-power wireless sensor network (winery)
This talk:
PETRAS project (EPSRC):
https://www.petrashub.org/
IoT in the Park:
Security vs. Adaptivity
Notes: Self-adaptive & self-organizing systems

## Slide 3: Overview
Motivation
Security of WSNs
Additional Info
‘Smart Cities’
WSNs in IoT
Threats Landscape
Defence Mechanisms
State of the Art
Our Research
Lack of Security

## Slide 4: Cites are becoming smarter
Image Source: datasciencebe.com
“By 2020, there will be 26 billion devices on IoT.”
Gartner
nyone
nything
nywhere
nytime
A
Examples:
Smart Santander
Manchester (City Verve)
Singapore
Amsterdam
Barcelona

## Slide 5: The Role of WSNs in IoT
Industrial IoT
Critical Infrastructure IoT
Smart Farming
Wireless Sensor Networks (WSNs)
“thousands of sensors (nodes) to sense the environment and modify it accordingly via actuation”
Mobility and heterogeneity of nodes
Suitable for the non-reachable places or harsh environmental conditions
Scalability to large scale of deployment
Adaptivity (new or failed nodes)
Centralized/distributed designs
Pros of WSNs

## Slide 6: How safe are we?
40%

## Slide 7: An example: WSN-based Water Infrastructure
Security is critical!

## Slide 8: Cons of WSNs
The biggest causality is that basically there is NO SECURITY! Not only that, there is a conflict between security and resiliency.
Attacker in the network
Depletes energy
Affects networking
Denies the service
Resource restricted nodes
Accessible environments
DATA LEVEL REQUIREMENTS
  Integrity
  Confidentiality
  Anonymity
  Freshness
ACCESS LEVEL REQUIREMENTS
  Authentication
  Authorisation
  Accessibility
NETWORK LEVEL REQUIREMENTS
  Robustness
  Availability
  Self-organisation
  Time synchronisation
Notes: Authentication, integrity and confidentiality

## Slide 9: Security Threats in WSNs
Multi-Layer
Application Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Jamming,
Node tampering, Eavesdropping
Data integrity attack,
Energy drain attack,
Desyncronisation attack
Attacks on reliability,
Malicious code attack
Denial of service,
Man in the middle
Jamming,
Collision
Spoofing/replaying information,
Selective forwarding/black holes,
Sinkhole attack,
Sybil attack,
Node replication attacks,
Wormhole attack,
Hello flood attack
WSN Layered
Architecture
External vs. Internal Attacks

## Slide 10: Few examples… (1) External Attacks
Jamming
In Industrial Control System it could lead to Denial-of-Service.

## Slide 11: Few examples… (2) Internal Attacks
1
2
4
3
6
7
8
9
1
2
4
6
8
7
5
10
11
12
Selective forwarding
  Data loss
  Delay in data delivery
Wormhole Attack
  Non-optimal routing
  Sending packets to false destinations

## Slide 12: Up-to-date Work
There is a need for lightweight fully-distributed solution that autonomously adapts communication decisions based on attack localization -> SELF-HEALING
Preventive Security Solutions: SPINS, LEAP, TinySec, etc.
Intrusion Detection Techniques: ‘Watchdog’, LIDeA, SAID, MALADY, etc.
Response Systems: Kinesis
Notes: 1. Fail to halt intruders nor do they ensure continued network functionality upon their detection.
2. Fail to effectively respond to intrusions or recover from the attack to mitigate significant interruption.
3. Kinesis (security incident response based on the response policy defined by the base station) - Hidden node problem

## Slide 13: What we did?
Find simulation tool (implement attacks)
Propose the solution
Evaluate the solution (real-life experiments)
Evaluate the solution (simulation)
Analyze the effect of attacks

## Slide 14: Contiki
“Contiki is an open source operating system for the Internet of Things which connects tiny low-cost, low-power microcontrollers to the Internet.”
A selection of hardware:
Supports recent low-power wireless standards:
Cooja Network Simulator

## Slide 15: Cooja: Contiki Simulator & Emulator

## Slide 16: Internal Attacks Evaluation
Implementation: Contiki OS & Cooja (Contiki simulator)
Observations:
Each attack has it’s own signature wrt to the network performance.
Two groups:
1. attacks that introduce additional data → reduced PDR and increased E2E delay
2. attacks that reduce no. of packets → reduced PDR and reduced E2E delay.

## Slide 17: ANTILIZER: A Lightweight Algorithm for Self-Healing
STEP 1: TRUST-BASED ROUTING
Pairwise trust between a node and its neighbours based on the network performance.
Choose your routing paths accordingly.
Overcomes the falsified information.

## Slide 18: ANTILIZER: A Lightweight Algorithm for Self-Healing
STEP 2: AGENT-BASED DIAGNOSIS
Each attack has a signature.
Move agents randomly to find them and keep the history.
Upon an incident detection, report the attack to base station and adjust your routing decisions.

## Slide 19: Test-bed: FIT IoT (France) & QEOP

## Slide 20: FAILSAFE
Real WSN/IOT deployments that either experienced some, or ended in, failure, that were either hacked or attacked in a nefarious way.
The First ACM International Workshop on the Engineering of Reliable, Robust, and Secure Embedded Wireless Sensing Systems (as part of Sensys 2017)
http://wp.doc.ic.ac.uk/failsafe/
Submission Deadline, 15th August, 2017

## Slide 21: References
[1] A. Perrig, R. Szewczyk, J. Tygar, V. Wen, and D. E. Culler. Spins: Security protocols for sensor networks. Wireless Networks, 8(5):521– 534, 2002.
[2] S. Zhu, S. Setia, and S. Jajodia. Leap: Efficient security mechanisms for large-scale distributed sensor networks. In Proceedings of the 10th ACM Conference on Computer and Communications Security, CCS ’03, pages 62–72. ACM, 2003.
[3] S. Marti, T. J. Giuli, K. Lai, and M. Baker. Mitigating routing misbehavior in mobile ad hoc networks. In Proceedings of the 6th Annual International Conference on Mobile Computing and Networking, MobiCom ’00, pages 255–265. ACM, 2000.
[4] I. Krontiris, T. Giannetsos, and T. Dimitriou. Lidea: A distributed lightweight intrusion detection architecture for sensor networks. In Proceedings of the 4th International Conference on Security and Privacy in Communication Netowrks, SecureComm ’08, pages 20:1– 20:10. ACM, 2008.
[5] J. Ma, S. Zhang, Y. Zhong, and X. Tong. SAID: A Self-Adaptive Intrusion Detection System in Wireless Sensor Networks, pages 60–73. Springer Berlin Heidelberg, 2007.
[6] S. Krishnamurthy, G. Thamilarasu, and C. Bauckhage. Malady: A machine learning-based autonomous decision-making system for sensor networks. In 2009 International Conference on Computational Science and Engineering, volume 2, pages 93–100, 2009.
[7] S. Sultana, D. Midi, and E. Bertino. Kinesis: A security incident response and prevention system for wireless sensor networks. In Proceedings of the 12th ACM Conference on Embedded Network Sensor Systems, SenSys ’14, pages 148–162. ACM, 2014.

## Slide 22
THANK YOU FOR
YOUR ATTENTION!