## Slide 1: RIFT: ROUTING IN FAT TREES
Krzysztof Grzegorz Szarkowicz
PLM, kszarkowicz@juniper.net

## Slide 2
This is a Introductory Material Based on Current Open Standards (Drafts)
None of those Things Constitute Commitments to Product Specifications, Offerings or Release Dates by Juniper at this Point in Time
Disclaimers and Expectations

## Slide 3
Introduction to DC Fabric Routing
Automatic Disaggregation
RIFT Introduction
Zero Touch Provisioning (ZTP)
North Flooding Reduction
Weighted Bandwidth Load Balancing (and more features)
Summary

## Slide 4: DC Fabric: Trends
Hyper-scalers are Establishing the Things to Come
  Vast Amount of Bandwidth Close to Producer & Consumer Necessary
    IP Fabrics in DC (Server Farms)
    Metro (Caches)
  Those Topologies are Becoming Uniform, Local and Regular
  WAN-Style Traffic Engineering & Protection Replaced by Wide Fan-Out & Distributed Systems Redundancy (Rather Than Chassis & FRR)
IP Fabric is Becoming the New “RAM Chip” to Consume Bandwidth
  No’one Configures RAM Banks and CAS/RAS Manually in Every Laptop
  IP Fabrics HW is Largely Commodity Already
  IP Fabrics Will “OPEX Commoditize”
Customers are Hosting Their Content & Critical Business Processes
  Hybrid Cloud for Many Reasons, One of Them to Keep Real-Estate from Hyper-scalers
  Need to Build Own Fabrics
  Impossible to Sustain Proprietary OPEX Efforts

## Slide 5: DC Fabric: Clos Topologies
Clos offers well-understood blocking probabilities
Work done at AT&T (Bell Systems) in 1950s for crossbar scaling
Fully connected CLOS is dense and expensive
Data centers today tend to be variations of “folded Fat-Tree”:
  Input stages are same as output Stages
  CLOS w/ (m >= n)
2_Rx X 2_Tx
2 (2_Rx X 2_Tx)

## Slide 6: DC Fabric: Routing Protocol Challenges
Current routing protocols are geared towards
  Irregular network topologies
  Low degree of connectivity
DC Fabric
  Typically regular topology (CLOS, folded Fat-Tree)
  Very high degree of connectivity (hyper-scale DCs)
No perfect match between current routing protocols and DC Fabric
  Routing protocols are complex (to deal with irregular topologies)
  Routing protocols are
    Fast, but not scalable to 100k nodes (link-state)
    Slow, when scalable to 100k nodes (distance-vector)

## Slide 7: Routing Protocol Review Link State & SPF = Distributed Computation
Advantages
  Topology elements - nodes, links, prefixes
  Each node originates packets with its elements
  Packets are ”flooded” across the network
  ”Newest” version wins
  Each node “sees” whole topology
  Each node “computes” reachability to everywhere
  Conversion is very fast
Disadvantages
  Every link failure shakes whole network
  Flooding generates excessive load for large average connectivity
  Periodic re-flooding (refreshes)
Examples: OSPF, IS-IS, PNNI, TRILL, RBridges

## Slide 8: Routing Protocol Review Distance/Path Vector = Diffused Computation
Prefixes “gather” metric when passed along links
Each node computes “single best” result and passes it on (Add-Path added “multiple best” results )
A node keeps all copies, otherwise it would have to trigger “re-diffusion”
Loop prevention is easy on strictly uniformly increasing metric.
Ideal for “policy” rather than “reachability”
Scales when properly implemented to much higher # of routes than Link-State
Slow convergence
Examples: BGP, RIP, IGRP

## Slide 9: Link State vs Distance/Path Vector
Link State
  Topology view  TE enabler
Distance/Path Vector
  Every computation could enforce policy – granular control – TE
Both protocols types (LS and Distance/Path Vector) are frequently used in todays networks
time
time
Node 1
Node 0
Node 3
Node 2
Node 5
Node 4
Node 1
Node 0
Node 3
Node 2
Node 5
Node 4
computation
Update tx-mission
Link State Convergence
Distance Vector Convergence

## Slide 10: DC Fabric Routing: Current State of Affairs
Several of Large DC IP Fabrics Use E-BGP with Band-Aids as De-Facto IGP (RFC7938) and Lots of Provisioning
  Numbering Schemes to Control “Path Hunting”
    ”Looping Paths” (allow-Own-as Under AS Private Numbering)
    “Relaxed Multi-Path ECMP” Since ECMP over Different AS in EBGP Does Not Work Normally
  Add Paths to Support Multi-Homing, N-ECMP, Prevent Oscillations
  Efforts to Get Around 65K ASes and Limited Private AS Space
  Proprietary Provisioning and Configuration Solutions, LLDP Extensions
  “Violations” of FSM Like Restart Timers and Minimum-Route-Advertisement Timers
  Emerging Work for “Peer Auto-Discovery” and “SPF” Diametrically Opposite to BGP Design Principles
  Reliance on “Update Groups” ~ Peer Groups to Prevent Withdrawal and Path Hunting After Server Link Failures
Others Run IGP (ISIS)
Yet Others Run BGP over IGP (Traditional Routing Architecture)
Less Than More Successful Attempts @ Prefix Summarization, Micro- and Black-Holing
Metros & Building Cabling Seems to Move towards Clos Variants
In Summary: High OPEX Solutions Not Necessarily Viable for Customers Who Cannot or Do Not Want to Build Sophisticated Talent Pool & Proprietary Solutions to Deal with Their Fabrics
  Fabric Director is _One_ Way to Approach That but Preconditions Controller
  Providing a “Distributed Routing and Configuration” Out-the-Box is _Another_ Way

## Slide 11: DC Fabric Routing Requirements
Problem / Attempted Solution | BGP modified for DC (RFC7938+ “mods”) | ISIS modified for DC (RFC7356 + “mods”) | RIFT Native DC
Link Discovery/Automatic Forming of Trees/Preventing Cabling Violations | ⚠️ | ⚠️ | ✓
Protocol Built-In Node Auto-Configuration (Zero Touch Provisioning – ZTP) | ✘ | ✘ | ✓
Minimal Amount of Routes/Information on ToRs/Leafs (cost optimized ToRs/Leafs) | ✘ | ✘ | ✓
High Degree of ECMP (BGP needs lots knobs, memory, own-AS-path violations) | ⚠️ | ✓ | ✓
High Degree of Non-ECMP, ECMP independent Anycast | ✘ | ✘ | ✓
Coarse northbound weighted bandwidth load balancing without TE | ✘ | ✘ | ✓
Basic Traffic Engineering by Prefix Attributes Modification (e.g. Next-Hops) | ✓ | ✘ | ✓
See All Links in Topology to Support Centralized Controllers for Advanced Traffic Engineering | ⚠️ | ✓ | ✓
Carry Opaque Configuration Data (Key-Value) Efficiently (Integrated Bootstrap) | ✘ | ⚠️ | ✓
Introduce to (Take a Node out of) Production Quickly and Without Disruption (Overload) | ✘ | ✓ | ✓
Automatic Disaggregation (with max. ECMP/N-ECMP) on Failures to Prevent Black-Holing | ✘ | ✘ | ✓
Minimal Blast Radius on Failures (On Failure Smallest Possible Part of the Network “Shakes”) | ✘ | ✘ | ✓
Fastest Possible Convergence on Failures | ✘ | ✓ | ✓
Unnumbered Links | ✘ | ✓ | ✓
Prefix Mobility | ✘ | ✘ | ✓
Simplest Initial Implementation | ✓ | ✘ | ✘

## Slide 12
Introduction to DC Fabric Routing
Automatic Disaggregation
RIFT Introduction
Zero Touch Provisioning (ZTP)
North Flooding Reduction
Weighted Bandwidth Load Balancing (and more features)
Summary

## Slide 13: RIFT: Novel Dynamic Routing Algorithm for Clos Underlay
General concept
Automatic cabling constraints
Automatic disaggregation on failures
Automatic flooding reduction
Other
“Just because the standard provides a cliff in front of you, you are not necessarily required to jump off it.”
— Norman Diamond

## Slide 14: RIFT At Glance: (2) Link-State Up, (3) Distance-Vector Down, (4) Bounce
(2) Link-State flood up (North)
  Full topology and all prefixes @ top spine only
(3) Distance Vector down (South)
  0/0 is sufficient to send traffic UP.
  More specific prefixes
    disaggregated in case of failure
    Policy Guided Prefix (PGP) for TE
(4) Bounce
  Flood reduction
  Automatic dis-aggregation

## Slide 15: Adjacency Formation (aka Hello)
Link Information Element
  POD #
  Level #
  Node ID
Transported over well known m-cast address and port
POD # == 0 “Any POD”
  Node derive POD from 1st Northbound neighbor it establish adjacency.
  Auto-configuration
Level # == 0 “Leaf”
Content
header
Major Ver.
Minor Ver.
System ID
Level
LIE
Name
Flood UDP port
Neighbor
POD#

## Slide 16: Automatic Topology Constraints
Automatic rejection of adjacencies based on minimum configuration
A1 to B1 forbidden due to POD mismatch
A0 to B1 forbidden due to POD mismatch (A0 already formed A0-A1 even if POD not configured on A0)
B0 to C0 forbidden based on level mismatch

## Slide 17: Topology Information Element
N-TIE := S-TIE + carries link-state info
  attributes
  Detailed topology
Not all fields always required
  Packing efficiency
  Contextual
TIE Types
  Node TIE
  Prefix TIE
  PGPrefix TIE (Policy Guided)
  KeyValue TIE (Bootstrap)
TIE packet
TIE element
NodeTIEElement
Prefixes
KeyValueTIEElement
Level
capabilities
flags
Set of NodeNeighborsTIEElement
Neighbour System ID
Level
Metric
Set LinkID
TIE Element
TIE header
TIE ID
Seq. Number
Lifetime
Direction (N/S)
Originator System ID
TIE Type
TIE Nr. Type
header
Major Ver.
Minor Ver.
System ID
Level

## Slide 18
Introduction to DC Fabric Routing
Automatic Disaggregation
RIFT Introduction
Zero Touch Provisioning (ZTP)
North Flooding Reduction
Weighted Bandwidth Load Balancing (and more features)
Summary

## Slide 19: Routing in steady state – basics
Leafs
  Only 0/0 to connected level 1 spines.
Spine 111 [112]
  0/0 via S31, S32 [S33,S34]
  Pfx A via L101
  Pfx B via L102
Spine 211 [212]
  0/0 via S31, S32 [S33,S34]
  Pfx C via L201
  Pfx D via L202
Spine 31, 32, 33, 34
  Pfx A via S111, S112
  Pfx B via S111, S112
  Pfx C via S211, S212
  Pfx D via S211, S212
S-TIE(111)
Neigh: 31, 32, 101, 102
Pfx: 0/0
111
N-TIE(201)
Pfx C
N-TIE(202)
Pfx D
N-TIE(212)
212
201
202
31
aggregation
localization
34
Pfx D
Pfx C
Pfx B
Pfx A
S-TIE(31)
Neigh: 111, 211
Pfx: 0/0
TIE(x) – TIE originated at node X.
211
112
101
102
32
33
One-hop
forwarding
Flooding

## Slide 20: S-TIE reflection
Spine @ level X [S31] sends S-TIE to node @ level (X-1) [S111]
Node @ level (X-1) [S111] sends S-TIE up to all neighbors [S32]
Spine that received bounced S-TIE [S32] compares their neighbors w/ one in S-TIE
Discovered “Equal connectivity group” used for
  Disaggregation
  Flood reduction
111
212
201
212
31
34
Pfx D
Pfx C
Pfx B
Pfx A
S-TIE(31)
Neigh: 111, 211
Pfx: 0/0
1
2
3
112
211
32
101
102
33

## Slide 21: Routing in failure – automatic disaggregation
101
102
Spine X [S32] receive bounced S-TIE(31)
Discovery
  Neighbor not matches – in S-TIE(S31) missing [S211] providing access to pfx: C, D
  Spine Y [S31] has no connectivity to some pfx (pfx: C, D).
  As node in lower level (Level 1) use 0/0 – risk of black hole/losses.
Spine X [S32] originate new S-TIE(32) w/ disaggregated prefixes (C,D)
Note:
Nodes on lower level (Level 1) get more specific route.
Nodes further down [L101, L102] still can use 0/0 only
111
212
201
202
31
Pfx D
Pfx C
Pfx B
Pfx A
S-TIE(31)
Neigh: 111
Pfx: 0/0
2
1
3
32
Pfx A S111
Pfx B S111
Pfx C S211
Pfx D S211
S-TIE(33)
Neigh: 111, 211
Pfx: 0/0; C, D
Pfx 0/0  S31, S32
Pfx C S32
Pfx D S32
Pfx 0/0  S31, S32
112
211

## Slide 22
Introduction to DC Fabric Routing
Automatic Disaggregation
RIFT Introduction
Zero Touch Provisioning (ZTP)
North Flooding Reduction
Weighted Bandwidth Load Balancing (and more features)
Summary

## Slide 23: Highly mesh topology
N-port spine switch
Level 2 spine – all N ports are southbound
Level 1 spine
  N/2 ports are Southbound
  N/2 ports are Northbound
Link-State Flooding become over-kill

## Slide 24: North Flooding without Reduction
A lot of redundant information
Known problem in Link-State protocols in Highly meshed networks
L
L+1
L+2

## Slide 25: North Flooding with Reduction
L
L+1
L+2
Each ‘L’ node knows from reflected S-TIEs of ‘L+1’ nodes, which ‘L+2’ nodes are reachable via particular ‘L+1’ node
It is enough, that single ‘L+1’ node reflects (floods) the N-TIEs from ‘L’ node to given set of ‘L+2’ nodes  Flood Repeater (FR) node
For redundancy, in RIFT ‘L’ node selects at least two ‘L+1’ nodes as FRs
  FRs are selected based on algorithm detailed in RIFT draft (Section 4.2.3.8)
N-TIEs sent to non-FRs marked with ‘do-not- reflect’ flag
Similar algorithm (not shown) is executed on ‘L+1’ nodes for the reflection at ‘L+2’ nodes towards ‘L+3’ nodes

## Slide 26
Introduction to DC Fabric Routing
Automatic Disaggregation
RIFT Introduction
Zero Touch Provisioning (ZTP)
North Flooding Reduction
Weighted Bandwidth Load Balancing (and more features)
Summary

## Slide 27: Zero Touch Provisioning
Automatic SystemID derivation
  RIFT SystemID (64 bits) is automatically derived from node’s EUI-64
  EUI-64 MA-L format is used, allowing organizationally governed 24 bits to be used to generate SystemID for multiple RIFT instances
Top level (superspine) switches must be manually configured either with flag=SUPERSPINE (default level 16), or an explicit level (e.g., level 3 in the example)
A node with non-configured level, derives it level from the neighbor’s level (highest neighbor’s level – 1)
  E, F  derived level 2
  I, J  derived level 1
Node with flag=LEAF_ONLY has always derived level 0
Level 3
Level 2
Level 1
Level 0
A
E
F
I
J
X
Y
Flag=LEAF_ONLY
Flag=LEAF_ONLY
Level=3
(manual)

## Slide 28
Introduction to DC Fabric Routing
Automatic Disaggregation
RIFT Introduction
Zero Touch Provisioning (ZTP)
North Flooding Reduction
Weighted Bandwidth Load Balancing (and more features)
Summary

## Slide 29: Weighted Bandwidth Load Balancing – No LINK FAILURE
Upstream node BW is determined as the BW to the upstream node + uplink BW of the upstream node
  On X, upstream node I  2 x 10G + 4 x 40G = 180G
  On X, upstream node J  2 x 10G + 4 x 40G = 180G
Upstream node BW is converted to next exponent of 2
  On X, upstream node I  180G  8 (Note: 27 < 180 < 28)
  On X, upstream node J  180G  8 (Note: 27 < 180 < 28)
  Here, both I and J upstream nodes are associated with exponent 8
Distance (metric) of the default route received from upstream node is adjusted (BAD – Bandwidth Adjusted Distance)
  BAD = original D * (1 + Max_Usptream_Exp – Current_Upstream_Exp)
  On X, upstream node I  BAD = D * (1 + 8 – 8) = D
  On X, upstream node J  BAD = D * (1 + 8 – 8) = D
   Equal BW load-balancing  distance (metric) not adjusted
100G
40G
10G
A
F
I
J
X
Y
E

## Slide 30: Weighted Bandwidth Load Balancing – LINK FAILURE
Upstream node BW is determined as the BW to the upstream node + uplink BW of the upstream node
  On X, upstream node I  2 x 10G + 2 x 40G = 100G
  On X, upstream node J  2 x 10G + 4 x 40G = 180G
Upstream node BW is converted to next exponent of 2
  On X, upstream node I  100G  7 (Note: 26 < 100 < 27)
  On X, upstream node J  180G  8 (Note: 27 < 180 < 28)
  Here, J upstream node has maximum exponent 8
Distance (metric) of the default route received from upstream node is adjusted (BAD – Bandwidth Adjusted Distance)
  BAD = original D * (1 + Max_Usptream_Exp – Current_Upstream_Exp)
  On X, default from upstream node I  BAD = D * (1 + 8 – 7) = D*2
  On X, default from upstream node J  BAD = D * (1 + 8 – 8) = D
  Weighted (BAD reciprocal) BW load-balancing  1/3 via I, 2/3 via J
100G
40G
10G
A
F
I
J
X
Y
E

## Slide 31: Weighted Bandwidth Load Balancing
Only default route load-balancing is influenced by BW changes upstream
  Disaggregated routes are not affected by default, but weighted BW load-balancing might be enabled for disaggregated routes as well
Change in bandwidth influences weighted BW load-balancing across maximum two levels
  Each level does it for itself & the level above (so it’s recursive, leafs start from the bottom)
  BW change between node A (level 3) and node X (level 2) doesn’t influence load-balancing at X (level 0)

## Slide 32: Moreover
Traffic engineering is included via “flooded distance vector overlay” including filtering policies like BGP  PGP (Policy Guided Prefix)
Special considerations for direct East-West forwarding
Packet formats are completely model based
Channel agnostic delivery, could be QUIC, TCP, UDP, UDT
Purging (given complexity) is omitted
Key-Value Store is supported (e.g. service configuration during flooding)
Overload bit (like Overload in IS-IS)
Lightweight RIFT version on leafs (only North RIFT, no South RIFT)  cheap leaf devices
Mobility

## Slide 33
Introduction to DC Fabric Routing
Automatic Disaggregation
RIFT Introduction
Zero Touch Provisioning (ZTP)
North Flooding Reduction
Weighted Bandwidth Load Balancing (and more features)
Summary

## Slide 34: Summary of RIFT Advantages
  Fastest possible convergence
  Automatic detection of topology
  Minimal routes on TORs
  High degree of ECMP
  Minimal blast radius on failures
  Fast De-comissioning of Nodes
  Reduced flooding
  Automatic neighbor detection
  Automatic disaggregation on failures
  Key-Value Store
  ZTP
Advantages of Link-State and Distance Vector
No disadvantages of Link-State or Distance Vector
And some neither can do

## Slide 35: STATUS
Standardization
  Initiated by Antoni Przygienda (Juniper Networks)
  Individual contribution to IETF Routing WG
  Standards Track Working Group Draft (I-D)
  Base for further work toward RFC
  draft-ietf-rift-rift-01
Implementation
  Prototype reference code exist
  PoC Test runs, performance data collected
Cooperation
  Join work at IETF WG (JNPR, CSCO, Nokia, Comcast)
  Contact authors, share opinion
  The data structures for packet are public (GPB)
I-D
RFC
STD
individual
Coming soon: IETF RIFT Hackaton
https://trac.ietf.org/trac/ietf/meeting/wiki/102hackathon
Champions: Tony Przygienda
When: Saturday and Sunday, July 14 and 15, 2018
Where: Fairmont Queen Elizabeth Montreal,
Remote participation possible

## Slide 36: Early Juniper Implementation
Packaged Pre-Production Code
  https://www.juniper.net/us/en/dm/free-rift-trial/
  Flooding/Hello/SPF/RIB/Flood Reduction
  Optional REDIS Analytics for Link-State DB, Routes and Statistics Implemented
Very Heavily Multi-Threaded to Fully Utilize Modern CPU Architectures
  Memory and Thread Safe Unlike C
Carries Its Own Topology Environment for Heavy-Duty Testing
Easily Portable Across All Modern OS Platforms (OSX, Linux)

## Slide 37: THANK YOU
kszarkowicz@juniper.net